## Slide 1
Routing Information Protocol

## Slide 2: Repetition: Basic Routing
Our approach so far:
  Next-hop routing
  Logical (IP) addresses
  Static Tables
This approach works only for small IP networks
We need to support dynamic large networks
A
C
D
E
F
B
R1
R2
R3
R4
N1
N2
N3
N4
N1, -
N2, R2
N3, R2 N4, R2

## Slide 3: Reachability and Metrics
The most fundamental functionality in a dynamic routing protocol:
  Find the ”best path” to a destination
Two algorithms in use to find best path
  Distance-Vector (Bellman-Ford)
  Link-state (Dijkstra)
But what is best path?
  Interior routing: typically number of hops, or bandwidth
  Exterior routing: business relations—peering
Metrics
  Number of hops (most common)
  Bandwidth, Delay, Cost, Load, ”Policies”

## Slide 4: Popular Routing Protocols
Routing Protocols
Routing Protocols
Interior
Interior
Exterior
Exterior
BGP
BGP
RIP
RIP
OSPF
OSPF
IS-IS
IS-IS
IGRP
(cisco)
IGRP
(cisco)
EGP
EGP

## Slide 5: Routing Information Protocol - RIP
RIP-1 (RFC 1058), RIP-2 (RFC 2453)
Metric is Hop Counts
  1: directly connected
  16: infinity
  RIP cannot support networks with diameter > 15.
RIP uses distance vector
  RIP messages contain a vector of hop counts.
  Every node sends its routes to its neighbours
  Route information gradially spreads through the network
  Every node selects the route with smallest metric.
RIP messages are carried via UDP datagrams.
  IP Multicast (RIP-2) or Broadcast (RIP-1)

## Slide 6: Distance Vector
A node advertizes its “distance- vector”
A list (vector) of all nodes that the node knows about
The distance to each of them
Advertizements are sent to neighbours only
Each neighbour updates its routing table and sends the new distance-vectors to its neighbours
  Bellman-Ford algorithm
3
a
c
b
d
e
2
1
1
1
2
4
Distance-vector from ”e”
{a, | 2} | {b, | 3} | {c, | 4} | {d, | 1} | {e, | 0}

## Slide 7: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 8: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 9
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 10
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 11: Example: Initial State
1
7
8
2
2
1
A
E
B
C
D
Info at node | A | Distance B C |  | to | Node D E | 
A B C D E | 0 7   1 | 7 0 1  8 |  1 0 2  |   2 0 2 |  | 1 8  2 0

## Slide 12: D sends vector to E
1
7
8
2
2
1
A
E
B
C
D
Info at node | A | Distance B C |  | to | Node D E | 
A B C D E | 0 7   1 | 7 0 1  8 |  1 0 2 4 |   2 0 2 |  | 1 8  2 0
Iʼm 2 from C, 0 from D and 2 from E
D is 2 away, 2+2< , so best path to C is 4

## Slide 13: B sends vector to A
1
7
8
2
2
1
A
E
B
C
D
Info at node | A | Distance B C |  | to | Node D E | 
A B C D E | 0 7   1 | 7 0 1  8 | 8 1 0 2 4 |   2 0 2 |  | 1 8  2 0
Iʼm 7 from A, 0 from B, 1 from C & 8 from E
B is 7 away, 1+7<  so best path to C is 8

## Slide 14: E sends vector to A
Iʼm 1 from A, 8 from B, 4 from C, 2 from D & 0 from E
1
7
8
2
2
1
A
E
B
C
D
Info at node | A | Distance B C |  | to | Node D E | 
A B C D E | 0 7   1 | 7 0 1  8 | 5 1 0 2 4 | 3  2 0 2 |  | 1 8  2 0
E is 1 away, 4+1<8
so C is 5 away, 1+2<
 so D is 3 away

## Slide 15: …until Convergence
1
7
8
2
2
1
A
E
B
C
D
Info at node | A | Distance B C |  | to | Node D E | 
A B C D E | 0 6 5 3 1 | 6 0 1 3 5 | 5 1 0 2 4 | 3 3 2 0 2 |  | 1 5 4 2 0

## Slide 16: Node Bʼ' ‘s distance vectors
1
7
8
2
2
1
A
E
B
C
D
Dest | Next hop A E C
A C D E | 7 9 6 12 12 1 10 10 3 8 8 5

## Slide 17: Handling Link Failure
1
7
8
2
2
1
A
E
B
C
D
Info at node | A | Distance B C |  | to | Node D | E
A B C D E | 0 7 8 10 12 | 7 0 1 3 5 | 8 1 0 2 4 | 10 3 2 0 2 |  | 12 5 4 2 0
A marks distance to E as  , and tells B
E marks distance to A as  , and tells B and D
B and D recompute routes and tell C, E and E
etc… until converge

## Slide 18: RIP ( Routing Information Protocol)
included in BSD-UNIX distribution in 1982
distance vector algorithm
  distance metric: # hops (max = 15 hops), each link has cost 1
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
from router A to destination subnets:

## Slide 19: RIP: example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B

## Slide 20: RIP: example
w
x
y
z
A
C
D
B
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement

## Slide 21: RIP: link failure, recovery
if no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly (?) propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 22: RIP Problem: Count to Infinity
1. Initially, R1 and R2 both have a route to N with metric 1 and 2, respectively.
N 1 -
N 1 -
N
N 2 R1
N 2 R1
R1
R2
2. The link between R1 and N fails.
x
N 1 -
N 1 -
N 2 R1
N 2 R1
N
3. Now R1 removes its route to N, by setting its metric to 16 (infinity).
N 16
N 16
N 2 R1
N 2 R1
N
4. Now two things can happen: Either R1 reports its route to R2. Everything is fine.
N 16
N 16
N 16
N 16
N
N 16
N 16

## Slide 23: RIP Problem: Count to Infinity
still has a route to N, advertises it to R1. Now things start to go wrong: packets to N are looped until their TTL expires!
N 3 R2
N 3 R2
N 2 R1
N 2 R1
N
N 2
N 2
R1
5. The other alternative is that R2, which
R2
Loop!
6. Eventually (~10-20s), R1 sends an update to R2. The cost to N increases, but the loop remains.
N 3 R2
N 3 R2
N 4 R1
N 4 R1
N
N 3
N 3
Loop!
7. Yet some time later, R2 sends an
update to R1.
N 5 R2
N 5 R2
N 4 R1
N 4 R1
N
N 4
N 4
Loop!
...
13. Finally, the cost reaches infinity at 16, and N is unreachable. The loop is broken!
N 16
N 16
N 16
N 16
N

## Slide 24: Solution1: Triggered Update
Send out update immediately
1
R Immediately announces the broken
link when it happens.
N 16
N 16
N 16
N 16
N
R1
R2
N 16
N 16
Triggered updates can cause excessive load on networks with limited capacity or networks with many routers on them.

## Slide 25: Solution 2: Split Horizon
R2, does not announce the route to N to R1 since that is where it came from.
N 16
N 16
N 2 R1
N 2 R1
N
Do not propagate information about a route over the same interface from which the route arrived.
Split horizon only prevents loops between adjacent routers
R1 R2
Eventually, R1 reports its route to R2 and everything is fine.
N 16
N 16
N 16
N 16
N
N 16
N 16

## Slide 26: Split Horizon Does Not Solve All Cases R2 R3
R1
X
N
R1 reports to R2 that N is unreachable
R2 believes that D is reachable through R3
R2 reports this to R1, who believes that N can be reached through R2....
Somewhat depending on timing.....

## Slide 27: Solution 3: Poison Reverse
Advertise reverse routes with a metric of 16 (i.e., unreachable).
Somewhat more aggressive variant of split horizon
– It handles some more error cases than split horizon
Eventually, R1 reports its route to R2 and everything is fine.
Limitation: Only works for “loop”s of size 2
N 16
N 16
N 16
N 16
N
N 16
N 16
2
R always announces an unreachable
route to N to R1.
N 16
N 16
N 2 R1
N 2 R1
N
R1
R2
N 16
N 16

## Slide 28: Solution 4: Hold Down
R1 ignores updates to N from R2 for some period of time.
N 16
N 16
N 2 R1
N 2 R1
N
N 2
N 2
When a route is removed, no update of this route is accepted for some period of time (hold-down time)- to give everyone a chance to remove the route.
R1 R2
N 16
N 16
N 16
N 16
N
N 16
N 16
Eventually, R1 sends the update to R2.
Limitation: Delays convergence

## Slide 29: Disadvantages with RIP
Slow convergence
  Changes propagate slowly
  Each neighbor only speaks ~every 30 seconds; information propagation time over several hops is long
Instability
  After a router or link failure RIP takes minutes to stabilize.
Hops count may not be the best indication for which is the best route.
The maximum useful metric value is 15
  Network diameter must be less than or equal to 15.
RIP uses lots of bandwidth
  It sends the whole routing table in updates.

## Slide 30: Why Use RIP?
After all these problems you might ask this question
Answer
  Because RIP is generally available
  It is simple to configure.